## Slide 1: The safe system approach in the Netherlands: adoption, implementation and lessons learned
Dr. Letty Aarts
Parachute webinar
26 September 2017

## Slide 2: International ranking
Source: IRTAD/OECD (2014)
WHO ranking of 180 states (2015)
  The Netherlands: rank 8
  Canada: rank 29

## Slide 3: Road safety figures

## Slide 4: Our traffic context
Dense population (>400 people/km2)…
…large traffic volumes
(> 2,000 mv/h on motorways)…
…many vulnerable road users (1.3 bicycles/inhabitant)…
…dense road network

## Slide 5: Historical development of safety visions
1900-1950
Individual blame culture:
- Bad luck (1900 )
- Accident-prone drivers (1920 )
1950-1985
Risks in man, road, vehicle:
- Single cause approach (1950 )
- Multiple cause approach (1960 )
1985 – now
Integral safe system approach
- Vision Zero
- Sustainable Safety

## Slide 6: Safe Traffic System and Vision Zero developments
Vision zero
Sustainable safety
Safe System approach Australia
Safe System approach New Zealand

## Slide 7
Sustainable Safety

## Slide 8: Sustainable Safety history
1992
Introduction of the Sustainable Safety vision
-2002
Start-up programme
1995
Start of demonstration projects
2005/2006
Launch of the
first advanced version
2017
Preparations for second advanced version

## Slide 9: Some words on the title
‘Sustainable’ as in UN Brundtland-report (1987) on sustainable development
“…a development that meets the needs of the present without compromising the ability of future generations to meet their own needs.”

## Slide 10: Core of Sustainable Safety - goals
Preventing crashes
Reducing probability of serious injury

## Slide 11: Core of Sustainable Safety – human measure
Humans are vulnerable
Humans are fallible
Humans are tempted

## Slide 12: Core of Sustainable Safety – proactive approach
Intervene as early in chain of events as possible
Prevent system failures
Make unsafe actions less dependent from individual choices

## Slide 13: How to deal with the ‘human measure’?
INFRASTRUCTURE
  Design fits to the human capabilities and limitations
VEHICLE
  Support the driving task
  Provide physical protection
ROAD USER
  Is well informed and trained
  Behaviour is being checked were needed
Engineering
Education
Enforcement
Notes: And it is then important to realize that although people make errors, that is not the same as that road users are to blame for crashes.
The road system should ideally be designed to expect and accomodate human error.
Design the road system to expect and accommodate human error, because it is inevitable that road users make mistakes and sometimes violate the law (and crashes occur)
tailor environment (road, vehicle) to human characteristics
prepare road user for traffic tasks (training, education)
    beware: not all training is beneficial -> e.g. skid training !
In a crash, interaction between vehicle – roadway – human body must be managed so that serious injury likelihood is minimized, if not eliminated

## Slide 14: Safety principles
Psychological
aspects of humans
Physical
aspects of humans
Functionality of roads
Predictability of road course and road user behaviour by recognizable road design
Homogeneity of masses, speed and driving directions
State awareness of road users
Forgivingness
of the road environment and of road users

## Slide 15: Functionality of roads
Road category | Flow | Exchange
Through road | all | -
Distributor road | road | intersection
Access road | - | all
Notes: 3 categories of road: Category 1) roads with through function for rapid movement of through traffic
Category 2 - Distributor roads for the distribution and collection of traffic between different districts and resd. areas
Category 3 - roads with an access function providing access to property whilst ensuring the safety of the street as a meeting place

## Slide 16: Homogeneity in mass, speed and driving direction
Prevention of conflicts at high speed (flow)
  Separate driving lanes for differences in mass or speed
  Opposite driving directions: physical separation
Conflicts unavoidable (exchange)? Reduce speed!
  Lower speed limit
  Speed reduction at intersections

## Slide 17: Forgivingness: physical and social
Physical forgivingness:
  Matted shoulders
  Obstacle-free zones
  Shielded obstacles
Social forgivingness:
  Anticipating way of traffic participation
  Giving space to other road users
  Particularly directed at less capable road users
Notes: Aim to mitigate the injury effects of crashes
Forgiving roadsides
Crash friendly obstacles
Road edge markings
Shoulder drop off treatments
etc

## Slide 18: Predictability of road layout and traffic behaviour
Reduce uncertainty and probability of failure:
  Recognizable situations: consistency in road design
  Predictable road course: continuity in road design
‘Essential Recognisability Characteristics ‘(ERC):
100 km/h
80 km/h
60/80 km/h
50 km/h
30 /15km/h
Notes: Aim to prevent uncertainty in use:
Avoid necessity to search for destination/directions
Ensure all road categories are recognisable (self explaining)
Limit the number of designs/road types and ensure uniformity in design

## Slide 19: State awareness of the road user
Being aware of ones own
  Competences
  Situational task capacibility
Chart: Age categories
| 0 - 5 year | 6 - 11 year | 12 - 14 year | 15 - 17 year | 18 - 19 year | 20 - 24 year | 25 - 29 year | 30 - 39 year | 40 - 49 year | 50 - 59 year | 60 - 64 year | 65 - 74 year | 75 +
Men | 29.5768 | 58.6951 | 97.2862 | 341.6983 | 189.3817 | 136.6828 | 80.5561 | 56.4829 | 45.665 | 41.1023 | 44.6854 | 78.4984 | 217.3446
Women | 18.1229 | 35.3165 | 79.1833 | 157.4235 | 92.6505 | 72.7312 | 49.8182 | 43.2883 | 40.6058 | 42.9986 | 54.7442 | 95.1275 | 190.1517
Notes: Ability of the road user to assess task capability for the driving task
Make road users aware of own capabilities and limitations
Teach road users to recognise dangerous situations and to manage risk
Become part of the solution, not the problem

## Slide 20
Implementation and results

## Slide 21: Demonstration projects
Aim: implementation experience at local level
Main lessons
  Cooperation between parties (road authorities + police)
  Transparency about tasks + budgets
  Communication (public support)

## Slide 22: Startup programme
Covenant (1997)
  central government, provincial, local authorities
  24 agreements on implementation and financing
Implemented measures:
  Categorisation of roads (ca. 100%)
  30 km/h zones: 30 000 km out of 55 000 km
  60 km/h zones: 12 500 km out of 25 000 km
  (Roundabouts: from 1000 to 3000)
  Essential Recognisability Characteristics (40-75% on rural roads)
  Increase in traffic enforcement (regional teams)
  Permanent traffic education toolkit: traffic education programmes for all age groups

## Slide 23: Total road safety effects
1600 to 1700 lives saved in 1998-2007
Decrease in risk was stronger than period before (5.8% versus 2.6% per year)
Benefits about 4x costs of measures
However: less effective for serious road injuries
Chart: Year
| 1987 | 1988 | 1989 | 1990 | 1991 | 1992 | 1993 | 1994 | 1995 | 1996 | 1997 | 1998 | 1999 | 2000 | 2001 | 2002 | 2003 | 2004 | 2005 | 2006 | 2007
continuation of decrease in risk scenario | 1371 | 1237 | 1311 | 1248 | 1150 | 1135 | 1122 | 1161 | 1223 | 1080 | 1044 | 1063.5093 | 1025.5762 | 1005.3458 | 996.7806 | 984.3134 | 1002.255 | 999.4845 | 1013.2335 | 962.4184 | 933.9855
actual development | 1371 | 1237 | 1311 | 1248 | 1150 | 1135 | 1122 | 1161 | 1223 | 1080 | 1044 | 985 | 969 | 973 | 893 | 905 | 902 | 744 | 685 | 668 | 638
Notes:   6% less deaths and hospitalizations

## Slide 24: Lessons learned in practice
Low cost implementation: phasing solution but not the final idea!
Start in the right order:
  Good network structure
  Well designed and attractive through roads
  Safe and credible lower order roads
Attention for:
  Communication with the public
  All elements of the road system
  Evaluation
Appropriate timing
Linkage to other policy domains to get support (integral approach)
Notes: Main issues about measures in the advanced version:
  Continuation of infrastructural measures
  Elaboration of education and enforcement as part of Sustainable Safety
  New possibilities through ITS
Policy issues:
  Build on the successes of the past (first phase of Sustainable Safety)
  More attention for systematic evaluation of effects
  Produce higher quality with similar amounts of effort
  More tuning, integration, and cooperation between fields

## Slide 25
New developments

## Slide 26: Elements for an update
Actual problems
Expected developments
Desired future
Goals
Context and conditions
Vision
= how to reach the desired future
Solutions

## Slide 27: Trends & developments
Demographic developments
Mobility patterns
Urbanisation
Information and communication technology
Global warming
Economic development

## Slide 28
Context and conditions:
Maintain the status quo
Only prevent damage to others
Inherently safe traffic for all (but realistic) = maximal safety
Desired future
Safety Accessibility Freedom
Enjoy the achievements
Coming to a rest
Economic activity
Care for children and the eldery
Development
Exploration of capabilities

## Slide 29
Elements for the new update
The human measure
The traffic system
Road functionality
Physical compatibility
Psychologic compatibility
Responsibility
Learning and innovation
Safety principles
Operationalisations
Measures
Goals:
Reduce largest risks
Prevent serious crashes
Limit the long-lasting consequences

## Slide 30: To conclude
First steps towards Safe System Approach: paradigm shift possible!
Success depends on understanding the vision behind it:
  Don’t wait for crashes to occur
  Real understanding of ‘the human measure’
  Start with the problem, then find sustainable solutions
Connect road safety to other policy domains
Join us towards a safe road traffic system
Share your ideas and experiences
Cooperate in taking first or further steps…

## Slide 31
Dr. Letty Aarts
I: www.swov.nl
E: Letty.Aarts@SWOV.NL
T: +31 70 317 33 79
Thank you for your attention!
Questions?